## Slide 1: PCB Routing
Tianxiao

## Slide 2: Routing
Don’t rely on Autorouter
  An aid to find bottleneck (at the position it fails to continue)
Ask for specification
  Minimum trace width (next page)
  Minimum trace spacing (at least 0.01mm)
Route with grid
  Snap grid 0.5mm for routing (depends on trace width)
  Avoid 90 degree trace angles
Leave room between traces and mounting holes
Power lines
  Create a ground plane
  Make power and ground traces wider
Silkscreen
  Wire, text, circle…
  Layer: 25 tNames, 26 bNames

## Slide 3: Routing
Trace width
  PCB trace width calculator link
  Thickness 0.035mm
  As wide as possible
5A 2.77mm
1A 0.3mm
0.1A 0.0125mm
0.01A 0.0005mm